Problem definition (physics + discretization)
Category	Setting / Value
Problem type	2D plane-strain Neo-Hookean elasticity (square domain)
Domain	([0, L] \times [0, L]), with (L = 1.0)
Mesh type	Structured quadrilateral mesh (2D square)
Mesh resolution	(N = 42) (42 × 42 grid; used by create_2D_square_mesh(L, N))
FE element	4-node quad, Neo-Hookean (NeoHookeMechanicalLoss2DQuad)
Gauss integration	num_gp = 2 (2×2 Gauss points per element)
Material model	Neo-Hookean, isotropic
Young’s modulus	(E = 1.0)
Poisson’s ratio	(\nu = 0.3)
BC type	Dirichlet on left/right boundaries for (U_x, U_y)
BC – left edge	(U_x = 0.0), (U_y = 0.0)
BC – right edge	(U_x = 0.1), (U_y = 0.1)
Control type	FourierControl (spatially varying stiffness field (K(x,y)))
Fourier x-frequencies	([2, 4, 6])
Fourier y-frequencies	([2, 4, 6])
Fourier z-frequencies	([0]) (effectively 2D)
Fourier amplitude scale	beta = 20
K field range	min = 1e-1, max = 1.0 (clamp of heterogeneity field)
Samples in dictionary	200 Fourier coefficient vectors (when generated via create_random_fourier_samples)

PI-FNO model & training hyperparameters (parametric/otf/transfer)
Category	Setting / Value
Operator model	FourierNeuralOperator2D
FNO modes (x)	modes1 = 6
FNO modes (y)	modes2 = 6
Channel width	width = 8
Network depth	depth = 4 residual blocks
Last projection channels	channels_last_proj = 32
Output channels	out_channels = 2 (displacement (u_x, u_y))
Output scaling	output_scale = 0.1
Total number of params	≈ 37,538 (printed in log)
FOL wrapper	PhysicsInformedFourierParametricOperatorLearning
Loss	Physics-informed Neo-Hookean FE residual (NeoHookeMechanicalLoss2DQuad)
Optimizer	Optax Adam, learning rate 1e-3
LR scheduler (unused here)	linear_schedule(1e-4 → 1e-5, transition_steps = 5000)
Max epochs	num_epochs = 5000
Convergence settings	relative_error = 1e-100, absolute_error = 1e-100 (effectively “epoch-based”)
Train batch size (param.)	batch_size = 5
Train indices	0–179 → 180 samples
Test indices	181–199 → 19 samples (sample 180 reserved for OTF)
Training plots	total_loss, residual_rms_batch_mean (physics residual RMS)
Train checkpoint	Least-loss checkpoint every 100 epochs → .../flax_train_state
Final state save	flax_final_state in the parametric output folder

### OTF fine-tuning & FE solver hyperparameters (slide 3: “OTF from param”)
OTF PI-FNO (starting from parametric weights)

Category	Setting / Value
Initial weights	Restored from parametric run: ./nn_output_mechanical_2D_neohooke_pi_fno_param/flax_train_state
OTF sample ID	otf_id = 180
Train set (OTF)	Only coefficient vector of sample 180 (shape (1 \times n_\text{coeffs}))
Test set (OTF)	Same as train: sample 180
parametric_learning flag	False (enables true on-the-fly mode)
Eval cases	eval_cases = [180]
Batch size (OTF)	batch_size = 1
Max epochs (OTF)	num_epochs = 5000
Convergence settings	Same: relative_error = 1e-100, absolute_error = 1e-100
Plots during OTF	total_loss, residual_rms_batch_mean saved in nn_output_mechanical_2D_neohooke_pi_fno_otf_from_param
Checkpoint directory (OTF)	./nn_output_mechanical_2D_neohooke_pi_fno_otf_from_param/flax_train_state

OTF- SLIDE 1
10 mins for training -2000 epochs

PARAMETRIC- SLIDE 2
30 mins for training – Auto Stopped between 3000-3500 epochs

PARAMETRIC TRANSFER LEARN- SLIDE 3.1
5 mins for training – Auto Stopped between 700-800 epochs

Absolute Error reduction = 0.005 − 0.0005 = 0.0045

Relative improvement = 0.0045 / 0.005 = 0.9 = 90%

PARAMETRIC - TRANSFER LEARN - SLIDE 3.2
-Dual phase heterogeneous sample
7 mins for training – Auto Stopped between 700-800 epochs

PARAMETRIC TRANSFER LEARN- SLIDE 3.3
-Dual phase heterogeneous sample with Circular inclusion
4 mins for training – Auto Stopped between 500-600 epochs

OTF_CIRCLE- SLIDE 4
-Dual phase heterogeneous sample with Circular inclusion

2025-12-10 20:47:35 - Info : pi_fno_pr_learning.Train - train checkpoint settings:{'least_loss_checkpointing': True, 'least_loss': inf, 'frequency'
…..
2025-12-10 20:52:12 - Info : mechanical_loss_2d.ComputeJacobianMatrixAndResidualVector - finished in 0.7253 seconds
  9%| | EPOCHS : AT 1712/20000 [04:34<48:57, 6.23it/s, train_loss=0.00515, test_loss=0.0051 , 2025-12-10 20:52:10 , AUTO-STOPPED

OTF_CIRCLE- SLIDE 4

-Dual phase heterogeneous sample with Circular inclusion

2025-12-10 20:47:35 - Info : pi_fno_pr_learning.Train - train checkpoint settings:{'least_loss_checkpointing': True, 'least_loss': inf, 'frequency'
…..
2025-12-10 20:52:12 - Info : mechanical_loss_2d.ComputeJacobianMatrixAndResidualVector - finished in 0.7253 seconds